## Slide 1: using the Intel RealSense Depth Camera on the Raspberry Pi 5

## Slide 2: Installation
Intel github: https://github.com/realsenseai/librealsense
Instructions to install: https://github.com/dannyh147/Pi5-realsense
Also needed these installs:
  sudo apt install libxcursor-dev
  sudo apt install libxi-dev
  sudo apt install libudev-dev
  sudo apt install libusb-1.0-0-dev
  sudo apt-get install libxrandr-dev
  sudo apt-get install xorg-dev
  sudo apt-get install libxinerama-dev

## Slide 3: Run the RealSense Viewer
cd ~/librealsense/build/Release/
./realsense-viewer
Then turn on the depth camera & RGB camera on the left side

## Slide 4: librealsense python install
Python library install requires extra steps which are also in:
  https://github.com/dannyh147/Pi5-realsense
Despite the ‘sudo python setup.py install’ it does not seem to work unless you go to the specific folder and then run a script:
  cd ~/librealsense/wrappers/python/
  python python-tutorial-1-depth.py
    Or: python depth_test.py (*good example of getting a depth at a pixel X,Y)
Even the script needs to be in that folder since it needs to import that local folder’s version!
  Eventually should get the ‘setup.py install’ to work!