## Slide 1: Robot Operating System V2

## Slide 2: Features of Robot Operating System V2
Real-time support
Uses DDS (Data Distribution System)
  no central master controller
  Real-time deterministic execution w/low latency
  Can coordinate multiple robots over the network
Security features SROS: encrypted comm, authentication, etc.
Available on Linux, Windows, macOS, microcontrollers.

## Slide 3: Sending messages
rclpy is python client library
You can publish a message to start moving:
  ‘Twist’ with linear speed from 0.0 – 1.0
  Then publish another message to stop

## Slide 4: Getting telemetry data
Create subscription for your callback function:
  self.create_subscription(Float32, 'ultrasonic', self.ultrasonic_callback, 10)
Then you unpack the data from the msg param:
  def ultrasonic_callback(self, msg):
    distance = msg.data

## Slide 5: Template ROS robot based on Yahboom RaspBot
Code is in \embedded\RaspberryPi\ROS2_driver\
Mclumk_Wheel_Sports.py calculates motor speeds for Mechanum wheels
Raspbot_Lib.py is empty template to take commands
  The Yahboom robot works through calling I2C commands, but that all needs to be replaced
Mcnamu_driver_template.py is the main driver code for motors, servos, RGB, buzzer, sensors.