## Slide 1: Yahboom RaspBot V2 ROS

## Slide 2: How to login & call ROS commands
ssh pi@192.168.1.11 *get IP address from display
  username: pi password: yahboom
ROS v2 Humble is installed in a Docker container:
  # *Note it may ALREADY be running so call docker ps first to check!
  bash ~/docker_ros2.sh
  # Basic launch:
  ros2 launch yahboomcar_bringup bringup.launch.py
To call ros2 commands need to bring up a separate terminal but stay in the same Docker:
  # Run this to see the existing Docker instances running:
  docker ps
  # Then use the container ID or name to get into that existing instance:
  docker exec --it eager_wilbur bash
Then start calling ros2 commands (or ros scripts):
  # Might need to source the ROS environment:
  source /opt/ros/humble/setup.bash && source /root/yahboomcar_ws/install/setup.bash
  # Turn on the LED headlight to green:
  ros2 topic pub /rgblight std_msgs/msg/Int32MultiArray "data: [0, 255, 0]" --once

## Slide 3: Python script to change LED lightbar
from Raspbot_Lib import Raspbot
car = Raspbot()
car.Ctrl_WQ2812_brightness_Alone(1, 255, 0, 0) # LED 1 = red
car.Ctrl_WQ2812_brightness_Alone(2, 0, 255, 0) # LED 2 = green
car.Ctrl_WQ2812_brightness_Alone(3, 0, 0, 255) # LED 3 = blue
car.Ctrl_WQ2812_brightness_Alone(4, 255, 255, 0) # LED 4 = yellow

## Slide 4: Move robot forward at speed for duration:
# Move forward at certain rate:
ros2 topic pub /cmd_vel geometry_msgs/msg/Twist "linear:
x: 0.15
y: 0.0
z: 0.0
angular:
x: 0.0
y: 0.0
z: 0.0" --times 20 --rate 10
# then stop:
ros2 topic pub /cmd_vel geometry_msgs/msg/Twist "linear: {x: 0.0, y: 0.0, z: 0.0}" --once

## Slide 5: Move forward in python script:
import rclpy
from rclpy.node import Node
from geometry_msgs.msg import Twist
import time
# rclpy is the primary client library for ROS2!
rclpy.init()
node = Node('mover')
pub = node.create_publisher(Twist, 'cmd_vel', 1)
# Move forward
msg = Twist()
msg.linear.x = 0.15
pub.publish(msg)
time.sleep(2)
# Stop
msg.linear.x = 0.0
pub.publish(msg)
# Cleanup
node.destroy_node()
rclpy.shutdown()

## Slide 6: Python scripts to run robot commands:
# Because ‘docker run’ is called file changes are lost except for /root/temp which is mapped to /home/pi/temp
cd /root/temp
python3 move_forward.py
python3 LED_set_lights.py