## Slide 1: RC & Ardupilot

## Slide 2: ArduPilot Firmware
Firmware that runs on Flight Controller Hardware
  Used for GPS-based autonomous (or semi-autonomous) flights
  PX4 is an alternative but harder to use
Different versions: ArduPlane, ArduCopter, ArduRover, ArduSub, etc.

## Slide 3: Types of Flight Controller Hardware
Standard ‘PixHawk style’ has same connectors, so peripherals plug in easily
  RadioLink PixHawk – probably best quality, but many knock-offs
    RadioLink versions actually have 'RadioLink' printed on them
    RadioLink version works with
    Predessor was called APM
CubePilot Orange+ Cube
HolyBro
  PixHawk 6X standard set $325
  PixHawk 6C mini $
Matek Wing Boards
Omnibus
Linux-Based
3rd party hardware that does not look like the PixHawk-style

## Slide 4: Pixhawk Flight Controller
This is a ‘style’ of controller with standard connectors
  I have a PixHawk v2.4.8 but NOT a Cube
Stuff that needs to be plugged in:
  Receiver / Antenna
  Servos
  Telemetry – get in-flight real-time data back to controller
  GPS / GNSS (supports GPS, BDS, GLONASS, GALILEO, QZSS, IRNSS)
  Battery voltage adapter to Pixhawk-friendly voltages
  IMU (Inertial Measurement Units): accelerometers / gyroscopes / magnetometers
  Altitude: Barometer
  Air speed sensor
  Camera
  Lidar
  Buzzer for feedback
Connect via microUSB cable and hit ‘Connect’ button from Mission Planner
&& sshclient.IsConnected

## Slide 5: Alternative to using MissionPlanner on Pi to just get telemetry data from PixHawk
You can get telemetry data directly through the serial port on the PixHawk
  this works with the RadioLink PixHawk but maybe not with knock-offs
Use DroneKit python library to connect to PixHawk & interpret data
  DroneKit github:
  My version: C:\p\embedded\RaspberryPi\PixHawk\dronekit_joes
    dronekit_check_attitude.py just continually gets telemetry data
Types of telemetry data you can get:
  GPS location
  Battery percent
  Attitude: roll, pitch and yaw
  Velocity / Ground speed / Air speed
  Gimbal status
  Armed yes/no

## Slide 6
Power regulator
to give PixHawk-friendly
voltage
Buzzer for feedback
To GPS / GNSS ‘dome’
To motor ESCs / servos
RadioLink PixHawk v2.4.8
Firmware FMUv3
Connect to a receiver to also
control via joystick controller

## Slide 7: Power Adapter so Lipo battery can power the PixHawk as well as the motors (also available in XT60 style plug)

## Slide 8: PixHawk accessories
6-pin connector adapter, can also
get version that splits into single
wires to hookup serial connection
to Pi or Nvidia Nano.
Buzzer for audio feedback such
as when it’s 'armed'.
Safety button to turn
on/off motors or 'arm‘ it.
Servo cable.

## Slide 9: CubePilot Cube
Cube plugs into something that looks like PixHawk but actually says CubePilot on it as well
Orange+ is latest & greatest $350
  Cheaper mini purple version for ground vehicles
Original version of Cube was black and called a ‘PixHawk 2.1’ but the named changed to just ‘Cube’

## Slide 10: CubePilot Cube Orange+

## Slide 11: Ground Control Software
Mission Planner is most popular and easiest, but also:
    QGroundControl
    APM Planner 2
    could also run app from phone or tablet
Used to flash firmware onto the flight controller hardware
Used to monitor flight and control vehicle remotely
  Can use in combination with a joystick-type controller, but it’s possible to have no controller at all. The point is an autonomous flight plan, anyways.
  Can stop the flight and call back to home, etc.