## Slide 1: Raspberry Pi controlling devices

## Slide 2: Solenoid
Only needs GPIO pin
and 5V power from Pi.
12V power comes from
power supply / battery.
Power goes through solenoid
and out to 12V ground.
LED only goes on when
solenoid is activated.
LED does NOT go on
just when it has power (either
the 5V power from the Pi or
the 12V power from battery/supply.

## Slide 3: Solenoid – input pins may be regular or terminal blocks. The high power to the Solenoid are terminal blocks.
This end may have terminal blocks as well.
Pins determine whether it triggers on high 5V.

## Slide 4: Cheap stepper motors can be controlled with ULN2003 driver boards
LEDs will alternate back-and-
forth when stepper
motor is moving.
LEDs off otherwise (even when powered).
GPIOs 14,15,18,23  IN1-4
Also needs 5V power

## Slide 5: Bigger NEMA17 stepper motors must be controlled with A4988 or DRV8825 boards

## Slide 6: Connect to PixHawk
Power is split off
from LiPo battery
with adapter
TELEM2 connection
to Pi pins

## Slide 7: Getting info from the PixHawk
DroneKit has code to get telemetry data from the PixHawk
  \embedded\RaspberryPi\PixHawk\dronekit_joes\
  *note the readme.txt that has some manual fixes that need to be applied to the library files! Library code is dated and needs small fixes.
Also can do it through mavproxy:
  pip3 install mavproxy
  mavproxy.py --master=/dev/ttyAMA0 --baudrate 57600
  There is the MAVSDK-Python git repo that has some examples to run (after the mavproxy server is running)
  *gives error, not sure this is working