## Slide 1: SLAM – Simultaneous Localization and Mapping

## Slide 2: VSLAM
https://github.com/VSLAM-LAB/VSLAM-LAB
*I thought I installed this and had it working, but can’t find it.

## Slide 3: ORB-SLAM using WSL on Windows
Must run this from WSL or real Linux
Windows command line (as admin) to bind the RealSense cam first:
  usbipd list *note the busID for the RealSense cam
  usbipd bind --busid 1-3
  usbipd attach --wsl --busid 1-3
*Getting errors:
  The IMU part of the sensor is not passed thru from usbipd - *This is a known limitation of wsl!!
  Also getting segmentation fault – but that is fixable, just ask Claude.

## Slide 4: ORB-SLAM on native Linux
This is working now on the Linux w/RTX 4060
  Actually does NOT need a GPU to run, other than the display window
Using the D435i:
  cd ~/ORB_SLAM3
  ./Examples/Stereo-Inertial/stereo_inertial_realsense_D435i Vocabulary/ORBvoc.txt Examples/Stereo-Inertial/RealSense_D435i.yaml my_trajectory
*This will save a map as my_trajectory.txt
  *ORB-SLAM will NOT save the point cloud! That requires additional code!!
    Does this make it pointless? Or can the code be integrated into my own app?
  This can be viewed with a separate tool like evo or Open3D or Rviz
    pip install evo

## Slide 5: ORB-SLAM on Raspberry Pi 5? Orin Nano?
On Nvidia Jetson Orin Nano:
  Yes, at full performance!
  Has USB 3.2 ports
  Jetpack ships with OpenCV 4.x already – check version, though
  Pangolin viewer works fine with the Nano GPU
  Another option: Isaac ROS Visual SLAM – optimized for Nvidia Nano
Pi 5:
  Yes, but you will only get 10-20fps performance
  Things that will help performance:
    Disable the viewer
    Use fast SSD card
    Adequate cooling
  Pi 5 has USB 3.0 – will work, but maybe slower?

## Slide 6: rtabmap
github.com/introlab/rtabmap
Working on the Linux RTX4060 computer:
  Just run rtabmap from anywhere
    Need to select the RGBD camera D400 series first!
    Then select New Database
    Then select Play button
    it’s installed in /usr/local/bin/rtabmap but built from source in /home/big/rtabmap
rtabmap allows exporting 3D clouds in ply, pcd, and obj formats
  Also allows export of poses

## Slide 7: 3D point cloud formats
Format | Full Name | Type | Best For
.ply | Polygon File Format | Points + optional mesh, color, normal | Widest compatibility: works in MeshLab, Blender, CloudCompare, Open3D
.pcd | Points Cloud Data | Points only, binary or ASCII | ROS ecosystem and PCL tools
.obj | Wavefront OBJ | Mesh/triangles + texture | 3D modeling and rendering – Blender, Unity, Unreal (game engines)

## Slide 8: Thermal Camera: MileSeey
Code in \embedded\RaspberryPi\PyThermalCam
  Code modified to turn image upside down!