## Slide 1: AI Edge Computing

## Slide 2: Options
Pi with AI Hat+
  $70 for 26 TOPS
  Supports TensorFlow and PyTorch
  Shares Pi’s memory, usually 8GB
Nvidia Jetson Orin Nano 8GB (also have 4GB version)
  $250 for 40 TOPS
    Newer ‘Super’ version is 67 TOPS
    102 GB/s memory
Nvidia AGX Orin
  $1000-$1400 for 275 TOPS, but has 64GB RAM
Nvidia Jetson Thor
  $2800 for 2070 TFLOPS and has 128GB RAM
Nvidia DGX Spark $4000 for 1 petaFLOP and 128GB

## Slide 3: Pi AI: running object detection streaming video
rpicam-hello -t 0 --post-process-file /usr/share/rpi-camera-assets/hailo_yolov6_inference.json
Has these pre-trained models:
  hailo_pose_inf_fl
  hailo_scrfd
  yolov5/6/8 personface / segmentation / inference / pose
    pose shows stick figure on humans
    segmentation shows people & things outlined
  acoustic_focus
  annotate_cv
  face_detect_cv

## Slide 4: Pi AI: Uses Hailo-8L AI accelerator
Chatboard at: https://community.hailo.ai/
To use models on the Hailo HAT you need to convert the models over to the hailo format and use hailo’s software stack!
  Just running on Pi5 will do a few frames/second vs the hailo AI’s 25+ frames/second
Various github repos at: https://github.com/hailo-ai
  hailo-rpi5-examples:
    cd ~/hailo-rpi5-examples
    source setup_env.sh
    cd basic_pipelines
    python detection.py
  hailo_model_zoo:
    Under hailo_models:
      license_plate_detection – uses compiled neural net so not immediately obvious how to use outside the Pi Hat…
      license_plate_recognition
      vehicle_detection
  hailo-apps: has voice control of hardware and GenAI stuff

## Slide 5: Running YOLO darknet on Jetson Orin Nano
Latest version: https://github.com/hank-ai/darknet
  Follow the instructions to cmake it on Linux
  Install the pkg file it makes so you can run darknet from anywhere
On the Jetson Orin Nano it will use the GPU (on Pi it will NOT)
darknet detector test cfg/coco.data cfg/yolov7.cfg cfg/yolov7.weights coco/dog_bike_car.jpg
  This will return coordinates & class for dog, bike & truck
  *Still takes 2 seconds – I assume it can run faster when loaded once and then quickly run on each image/frame…

## Slide 6: Running YOLO darknet on the Pi AI HAT
https://github.com/hailo-ai/darknet
  Although it’s in the Hailo general repo this actually does NOT have anything to do with the Raspberry Pi AI HAT hailo module!!
    It was just forked from AlexeyAB/darknet and not really modified
To use YOLO darknet on the Pi’s hailo GPU would take a lot of work to convert over the model using hailo’s tools.
  The Pi can run it on the CPU, though