## Slide 1: My ROS2 robot based on YahBoom RasbBot

## Slide 2: Yahboom’s startup
Got rid of the startup scripts in /home/pi/.config/autostart/
  There was start_raspbot.desktop that started the Android app server
  Also start.desktop that started the OLED display driver

## Slide 3: Yahboom’s Ros docker container
Run using bash ~/docker_ros2.sh
The only Docker mounted volume is mapping the original /home/pi/temp to /root/temp
  That’s where my ROS2 scripts are currently
In the docker container the user is root (on the Pi it’s just pi user)

## Slide 4: My new Docker container for the BeagleBone:
bash ~/my_docker_ros2.sh
  ros2 launch my_robot_bringup bringup.launch.py
To get into the already-running docker instance:
  docker ps # get the docker name
  Run: docker exec -it fervent_chandrasekhar bash
To run some ROS2 scripts:
  cd ~/temp/embedded/RaspberryPi/ROS2_driver/ROS_scripts
  python3 move_forward.py

## Slide 5: My new ROS2 hardware driver for BeagleBone:
Robot_Lib.py:
  Makes SSH connection to BeagleBone
  Writes to /tmp/robot#.txt to control the BeagleBone motors & servos
robot_driver.py: hardware implementation
  Currently connects to BeagleBone through WiFi
*Current issues:
  *The slow down from 0.3 – 0.0 doesn’t seem to work.

## Slide 6: New docker container for Yahboom Rosmaster board:
bash ~/Rosmaster_run_docker.sh
# Need to specify the COM port:
ros2 launch my_robot_bringup bringup.launch.py com_port:=/dev/ttyUSB0

## Slide 7: My new ROS2 hardware driver for Rosmaster Yahboom Board V3
It creates a bot with:
  from Rosmaster_Lib import Rosmaster
  bot = Rosmaster(com="/dev/ttyUSB0")
*Need to modify it to adjust for motor polarity.